## Slide 1
Hardware III — Person 6 Role Fulfillment
Data Research + Narrative Owner Rafik El Khoury
Hardware III — IAAC MRAC/MAAI 2025/2026 | May 2026

## Slide 2
What Is Hardware III?
• Interactive table installation — visitors physically configure a small building scenario
• Overhead projector guides assembly through 5 construction phases in real time
• At the end: side-by-side LCA comparison of 3 construction methods + reclaimed brick baseline
• Tech stack: TouchDesigner FSM + Python/OpenCV (ArUco) + ESP32/RFID
• Team of 7, IAAC MRAC + MAAI — finals May 22, 2026
The political argument
• Turn abstract construction data into embodied knowledge: you build the comparison yourself
• The asymmetry in data confidence between methods IS the installation's core message

## Slide 3
Person 6 — My Role
Responsibilities
• Source LCA data for all 4 construction methods
• Structure data as ranges with source tiers — no unsourced fixed values
• Write method descriptions and phase texts for visitor-facing projection
• Define the comparison baseline (reclaimed brick)
Deliverables
• 4 CSV files in data/methods/ (one per method, phase × parameter × range × source)
• methods_db.json — corrected and populated for TouchDesigner to read
• Method descriptions, 5 phase texts, final comparison insight

## Slide 4
Research Foundation — What Was Already Done
• 7 deep-research strands completed using the earn-the-data discipline (docs/research_2/)
Each strand produced:
• VALUES.md — phase × parameter × value_low/high × unit × assumption × source × tier
• SYNTHESIS.md — evidence convergence, methodology wobbles, geographic gaps
• BIBLIOGRAPHY.md — full citations, tier classification
The gap I found:
• Research was complete but data had never been transferred into structured files
• data/methods/ directory was empty — 4 CSVs and methods_db.json were all placeholders
• My job was not more research. It was translation: research docs → structured data

## Slide 5
Geographic Strategy — Catalonia ▸ Spain ▸ EU ▸ Global
• Locked in Phase 2 docs: use the most local source available, flag the level
Tier 1 (Catalan/Spanish): BEDEC (ITeC), CYPE, Hispalyt EPDs
Tier 2 (Institutional/EU): European research, validated EPDs
Tier 3 (Vendor): Allowed only with a Tier 1/2 sibling row
Per-method geographic reality:
• Masonry — strong Catalan data (Hispalyt, BEDEC, CYPE) ✓
• 3D Printed — zero peer-reviewed Catalan LCA. Data: Qatar, Australia, US
• Prefab/CLT — no Spanish CLT mills. Data: Austrian/Swedish EPDs
• Reclaimed Brick — no Catalan tier-1 LCA. Data: Finland, Switzerland, UK
⚠ The geographic asymmetry between methods is not a flaw — it IS the argument

## Slide 6
Method Finding: Masonry
• Traditional fired-clay brick, hand-laid on site
CO₂ (A1–A3 cradle-to-gate)
• Structure: 32–75 kgCO₂e/m² wall — Hispalyt EPDs, Tier 1
• Whole building: 205–490 kgCO₂e/m² GFA — sanity check vs Izaola 2023, De Wolf 2017
Labour & Cost
• Labour: 22–34 h/m² — CYPE FEF010/FFZ010, Tier 1
• Cost: 950–1,350 EUR/m² — CYPE + BEDEC, Tier 1
• Time: 14–20 weeks
Data quality
• Only method with genuine Catalan tier-1 data from physical Spanish kilns
• BEDEC environmental column inherits Ecoinvent — not fully independent from Hispalyt EPDs

## Slide 7
Method Finding: 3D Printed Concrete
• Robotic concrete extrusion — structural walls only; all other phases are conventional
CO₂
• Wall element: 44–90 kgCO₂e/m² wall — Mohammad 2020 (Qatar), Tier 1
• Whole building: 58–147 kgCO₂e/m² GFA — Rossi 2024, Tier 1 (caveats: n=4)
• 3DP earth (cob): 12–25 kgCO₂e/m² wall — Alhumayani 2020, Tier 1
7 methodology wobbles documented:
• Cement content (±45%), reinforcement boundary (+30%), functional unit (wall vs GFA)
• Printer electricity, cob biogenic convention, durability assumption, geography
Critical gap
⚠ No published LCA for any Catalan 3DP project. IAAC TOVA exists in Collserola — no LCA published.
• Data transfers from Qatar/Australia to Barcelona context with explicit flag

## Slide 8
Method Finding: Prefab (Modular Concrete + CLT)
• Two sub-methods: volumetric modular concrete and cross-laminated timber (CLT)
CLT CO₂ (A1–A3)
• With biogenic carbon credit: 130–220 kgCO₂e/m² GFA
• Without biogenic credit: 220–350 kgCO₂e/m² GFA ← 30% swing on accounting choice
Modular concrete CO₂
• 280–569 kgCO₂e/m² GFA — Wei 2024 (Hong Kong typology), Tier 1
Catalonia-specific penalty most LCAs ignore:
• CLT Austria→Barcelona ≈ 1,800–2,200 km road = adds 25–60 kgCO₂e/m² GFA
⚠ No Spanish CLT mills exist. No Spanish modular concrete primary LCA.
• Data from Hong Kong, Austria, Sweden — flagged as EU proxy

## Slide 9
Method Finding: Reclaimed Brick (Baseline)
• Salvaged fired-clay brick, cleaned and relaid. Role: comparison BASELINE, not a competitor
The load-bearing finding — same wall, same bricks, 3 different accounting rules:
• Cut-off (default): 8–25 kgCO₂e/m² GFA
• Avoided-burden: 18–45 kgCO₂e/m² GFA
• System-expansion (50/50): 35–70 kgCO₂e/m² GFA
• That is a 5× swing. Every published LCA makes this choice without always saying so.
Labour
• 2–4× higher than new brick (cleaning + sorting + hand-fitting variable dimensions)
Geographic gap
⚠ No Catalan tier-1 LCA. BEDEC has no reclaimed-brick entry as of 2026.
• Data from Finland (Salmio & Huuhka 2026), Switzerland (Re:Crete, K.118), UK (RBC EPD)

## Slide 10
Files Delivered
CSVs (data/methods/)
methods_db.json
• masonry.csv — 25 rows, Tier 1 Catalan
• 3d-printed.csv — 33 rows, global + gap flag
• prefab.csv — 38 rows, CLT + modular
• reclaimed-brick.csv — 25 rows, 3 allocation siblings
• Schema: phase, parameter, value_low,
• value_high, unit, assumption,
• source, source_tier
• All UNKNOWN cells marked explicitly
• 4 correct method names (was: Cantilever/Arch/Truss)
• LCA summary fields per method
• co2_per_m2_range, labor_hours_range,
• time_range, cost_per_m2_range
• source_label + geographic_tier
• Link to CSV per method
• 5 phase texts (Foundation→Finishing)
• Final comparison insight (3 paragraphs)
• ⚠ RFID tags: placeholders — Person 7 must assign

## Slide 11
Narrative Decisions
Tone decision (resolved with team)
• Scientific, neutral, factual — not storytelling, not advocacy
• Each description states what the method is, where the data comes from, key number
Example — Masonry:
• "Load-bearing fired-clay brick, hand-laid on site. Catalan tier-1 data: Hispalyt EPDs, BEDEC (ITeC), CYPE. CO₂: 205–490 kgCO₂e/m² GFA. Labour: 22–34 h/m²."
Example — 3D Printed:
• "Robotic concrete extrusion. Structural walls only — foundation, roof, openings conventional. No published LCA for any Catalan project. Data from Qatar, Australia, US. CO₂: 58–147 kgCO₂e/m² GFA."
Phase texts (5 lines, one per construction phase)
• Functional, consistent across methods — appear during PHASE_N states in the FSM

## Slide 12
Is This a Strong Idea? — Assessment
STRENGTHS
• Earn-the-data discipline: tiered sourcing, no unsourced fixed values, ranges throughout
• Catalan-first geography: honest about what local data exists vs. what is a proxy
• The 5× reclaimed brick swing is intellectually honest and more interesting than a single number
• Data asymmetry between methods (masonry = real Catalan; 3DP = Qatar) IS the argument
• Methodology wobbles documented — the installation can show uncertainty, not false precision
CONCERNS
⚠ May 22 = 12 days. CSVs just written — not yet tested in TouchDesigner.
⚠ 3 out of 4 methods have no Catalan primary LCA — honest, but will need clear UI flagging
⚠ RFID tags still placeholder — hardware dependency on Person 7 before demo
• Comparison view visual design not yet confirmed — data is ready; display is not
VERDICT
• Strong idea, methodologically serious. Risk is time, not quality of the argument.

## Slide 13
Outstanding Flags (Not Person 6)
For Person 7 (Hardware/Sensors):
⚠ RFID tag IDs in methods_db.json are placeholders — read physical tags, update JSON
For the team (integration):
• Switch working branch to master — all Person 6 files are on treethreetree branch
• Test CSV reads in TouchDesigner before May 22
For the projection design:
• Methodology wobble overlay must surface: allocation rule for reclaimed brick,
• biogenic carbon toggle for CLT, geographic source disclosure for 3DP and prefab
For Person 6 (if time allows):
• Strand 07 (Spanish/Catalan superpowers) was still running — check if outputs added anything
• Consider a SOURCES.md in data/ listing all 9 attribution corrections from data-inventory.md